## Slide 1
YahBoom Croco:Kit tutorial
Lesson 26
DIY coures（4）
Smart cooling fan
Advanced course

## Slide 2
Content
YahBoom Croco:Kit tutorial
Part 5
Part1
Learning goals
Part 2
Preparation
Part3
Connection
Part 4
Search for blocks
Combine blocks
Advanced course

## Slide 3
Part 1
YahBoom Croco:Kit tutorial
After downloading the program, we can see the word 'Happy Birthday!' on the Micro:bit LED dot matrix. Then, Micro:bit LED dot matrix will display “heart”.
The fan automatically adjusts the speed according to the ambient brightness. The brighter the ambient brightness, the faster the fan speed.
A button can turn on the fan and B button can turn off the fan.
Learning goals
Advanced course

## Slide 4
Part 2
YahBoom Croco:Kit tutorial
Hardware:
● 1 X Micro:bit Board
● 1 X Micro USB Cable
● 1 X Diamond breakout
● 1 X Photosensitive module
● 6 X Alligator clip
● 1 X Motor drive module
● 1 X PC
Mode 1 online programming: First, we need to connect the micro:bit to the computer by USB cable. The computer will pop up a USB flash drive and click on the URL in the USB flash drive: http://microbit.org/ to enter the programming interface. Add the Yahboom package: https://github.com/lzty634158/Croco-Kit to program.
Mode 2 offline programming: We need to open the offline programming software. After the installation is complete, enter the programming interface, click【New Project】, add Yahboom package: https://github.com/lzty634158/Croco-Kit , you can program.
Preparation
Advanced course

## Slide 5
Part 2
YahBoom Croco:Kit tutorial
Preparation
! ! !Note: S1 be set to the ON, S2 be set to the IO, and S3 to the NC.
Advanced course

## Slide 6
Part 3
YahBoom Croco:Kit tutorial
Connection
Expansion board | Photosensitive Module | Motor drive module
P0 | OUT | 
P1 |  | M2
3.3V | VCC | 
5V |  | VCC
GND | GND | GND
Advanced course

## Slide 7
YahBoom Croco:Kit tutorial
Part 4
Search for blocks
Advanced course

## Slide 8
YahBoom Croco:Kit tutorial
Part 4
Search for blocks
Advanced course

## Slide 9
YahBoom Croco:Kit tutorial
Part 4
Search for blocks
Advanced course

## Slide 10
Part 5
YahBoom Croco:Kit tutorial
Combine blocks
Advanced course

## Slide 11
YahBoom Croco:Kit tutorial
Thank you ！
Powered by YahBoom
Advanced course