## Slide 1
YahBoom Croco:Kit tutorial
Lesson 30
DIY coures（8）
DIY Accordion
Advanced course

## Slide 2
Content
YahBoom Croco:Kit tutorial
Part 5
Part1
Learning goals
Part 2
Preparation
Part3
Connection
Part 4
Search for blocks
Combine blocks
Advanced course

## Slide 3
Part 1
YahBoom Croco:Kit tutorial
After downloading the program, you can see the microbit LED dot matrix display ‘Hello!’,we can put our hand in front of the ultrasonic module, when the ultrasonic module detects different distances, buzzer will play different tones, the effect of playing the piano by hand can be achieved.
Learning goals
Advanced course

## Slide 4
Part 2
YahBoom Croco:Kit tutorial
Preparation
Hardware:
● 1 X Micro:bit Board
● 1 X Micro USB Cable
● 1 X Diamond breakout
● 4 X Alligator clip
● 1 X Ultrasonic module
● 1 X PC
Mode 1 online programming: First, we need to connect the micro:bit to the computer by USB cable. The computer will pop up a USB flash drive and click on the URL in the USB flash drive: http://microbit.org/ to enter the programming interface. Add the Yahboom package: https://github.com/lzty634158/Croco-Kit to program.
Mode 2 offline programming: We need to open the offline programming software. After the installation is complete, enter the programming interface, click【New Project】, add Yahboom package: https://github.com/lzty634158/Croco-Kit , you can program.
Advanced course

## Slide 5
Part 2
YahBoom Croco:Kit tutorial
Preparation
! ! !Note: S1 be set to the ON, S2 be set to the IO, and S3 to the FM.
Advanced course

## Slide 6
Part 3
YahBoom Croco:Kit tutorial
Expansion board | Ultrasonic Module
P1 | TRIG
P2 | ECHO
3.3V | VCC
GND | GND
Connection
Advanced course

## Slide 7
YahBoom Croco:Kit tutorial
Part 4
Search for blocks
Advanced course

## Slide 8
YahBoom Croco:Kit tutorial
Part 4
Search for blocks
Advanced course

## Slide 9
Part 5
YahBoom Croco:Kit tutorial
Combine blocks
Advanced course

## Slide 10
YahBoom Croco:Kit tutorial
Thank you ！
Powered by YahBoom
Advanced course
Advanced course